## Slide 1
Biocarbon Stability Standards - A Short Review Hydrochar Stability Workshop
Jeremy Taylor Chief Technology Officer
SoMax Circular Solutions July 17, 2025

## Slide 2: Agenda
Overview of Key Standards and Methodologies
How Stability is Measured Across Frameworks
Hydrochar Limitations with Current Evaluation Methods

## Slide 3: Standards and Methodologies
ASABE X### – Method of Measurement and Testing of Biochar
  Active Development – Not Published
  ASABE – American Society of Agriculture and Biological Engineers
  U.S. based standard
ISO 17### – Pyrogenic Biocarbon
  Active Development – Not Published
  ISO – International Organization for Standardization
Puro.earth – Terrestrial Storage of Biomass – Methodology for CO2 Removal
  Published and Available for Carbon Removal Credits
  Woody Biomass Burial or Storage

## Slide 4: ASABE – Method of Measurement and Testing of Biochar
Core focus is Biochar for ‘carbon preserving purposes’
  Excludes energy or industrial applications
  Includes all feedstocks
Permanence assessed with three methods:
  H/Corg Molar Ratio -
  O/Corg Molar Ratio -
  Random Reflectance – Per ISO 7404-5
    Methods for the petrographic analysis of bituminous coal and anthracite – Part 5: Method of determining microscopically the reflectance of vitrinite

## Slide 5: ISO – Pyrogenic Biocarbons
Core focus is Biocarbons for Agricultural and Industrial Applications
  Excludes fuel energy applications
Permanence assessed with three methods:
  Inertinite Content – ISO 7404-5: Methods for the petrographic analysis of bituminous coal and anthracite – Part 5: Method of determining microscopically the reflectance of vitrinite
  H/Corg Molar Ratio – ISO 16948: Solid biofuels — Determination of total content of carbon, hydrogen and nitrogen
  Fixed Carbon – ISO 21626-1: Soil improvers and growing media — Biochar — Part 1: Requirements and characteristics

## Slide 6: ISO – Carbon Stability
Property Term | Unit | Class 1 | Class 2 | Class 3 | Class 4 | Class 5
Inertinite | % of organic carbon in mass |  95 | 90 – 95 | 85 – 90 | 75 – 85 | 75
H/Corg | Molar ratio | 0.4 | 0.4 – 0.5 | 0.5 – 0.6 | 0.6 – 0.7 | 0.7
Fixed Carbon | % in mass |  90 | 85 – 90 | 80 – 85 | 70 – 80 | 70

## Slide 7: Puro.earth – Terrestrial Storage of Biomass

## Slide 8: Puro.earth – Terrestrial Storage of Biomass
Core focus is long term storage (>100 years) of wood or woody biomass.
  Requirements: Eligible Feedstock – Woody or woody biomass with rigid physical structure and high lignin content
  C:N Mass Ratio – Higher than 80*
    *Unless the storage reliably excludes liquid water, such as under permanently frozen or dry (xeric) conditions

## Slide 9: Hydrochar Limitations with Current Frameworks
Property Term | Unit | Class 5 / Or Standard | Hydrochar Upper Range | Hydrochar Typical Range
Inertinite | % of organic carbon in mass | 75 | Unknown | Unknown
Fixed Carbon | % in mass | 70 | 45 – 50 | 15 – 30
H/Corg | Molar ratio | 0.7 | 0.85 – 0.9 | 1.2 – 1.4
O/Corg | Molar ratio | 0.2 | 0.15 – 0.2 | 0.2 – 0.4
C/N | Mass ratio | 80 | 70 – 100 | 15 – 20

## Slide 10: Conclusions
Hydrochar typically does not meet the requirements for carbon permanence and stability
Terrestrial Storage shows the most potential to use Hydrochar as a carbon sequestration media.
Industries seem to write standards that fit their specific product.
Jeremy@somaxhtc.com